## Slide 1: Computer Vision CSE 455 Edges and Lines Linda Shapiro Professor of Computer Science & Engineering Professor of Electrical Engineering

## Slide 2: Convolution: Weighted sum over pixels

## Slide 3: Filters

## Slide 4: Cross-Correlation vs Convolution

## Slide 5: Cross-Correlation vs Convolution
Do this in HW!

## Slide 6: Cross-Correlation vs Convolution
These come from signal processing and have nice mathematical properties.

## Slide 7: So what can we do with these convolutions anyway?
Mathematically: all the nice things
Commutative
  A*B = B*A
Associative
  A*(B*C) = (A*B)*C
Distributes over addition
  A*(B+C) = A*B + A*C
Plays well with scalars
  x(A*B) = (xA)*B = A*(xB)
BUT WE TEND TO USE CORRELATION BECAUSE OUR FILTERS ARE SYMMETRIC, AND THEN WE JUST CALL IT CONVOLUTION!

## Slide 8: So what can we do with these convolutions anyway?
This means some convolutions decompose:
2D Gaussian is just composition of 1D Gaussians
  Faster to run 2 1D convolutions
= +

## Slide 9: So what can we do with these convolutions anyway?
Blurring
Sharpening
Edges
Features
Derivatives
Super-resolution
Classification
Detection
Image captioning
...

## Slide 10: So what can we do with these convolutions anyway?
Blurring
Sharpening
Edges
Features
Derivatives
Super-resolution
Classification
Detection
Image captioning
...
Much of low-level computer vision
is convolutions
(basically)

## Slide 11: What’s an edge?
Image is a function.
Think of the gray tones as HEIGHTS.
Edges are rapid changes in this function

## Slide 12: What’s an edge?
Image is a function
Edges are rapid changes in this function

## Slide 13: Finding edges
Could take derivative
Edges = high response

## Slide 14: Image derivatives
Recall:
We don’t have an “actual” function, must estimate
Possibility: set h = 1
What will that look like?

## Slide 15: Image derivatives
Recall:
We don’t have an “actual” Function, must estimate
Possibility: set h = 1
What will that look like?

## Slide 16: Image derivatives
Recall:
We don’t have an “actual” Function, must estimate
Possibility: set h = 2
What will that look like?

## Slide 17: Image derivatives
Recall:
We don’t have an “actual” Function, must estimate
Possibility: set h = 2
What will that look like?

## Slide 18: Images are noisy!

## Slide 19: But we already know how to smooth
* =

## Slide 20: But we already know how to smooth
* =

## Slide 21: Smooth first, then derivative

## Slide 22: Smooth first, then derivative

## Slide 23: Smooth first, then derivative

## Slide 24: Smooth first, then derivative

## Slide 25: Smooth first, then derivative

## Slide 26: Smooth first, then derivative

## Slide 27: Smooth first, then derivative

## Slide 28: Smooth first, then derivative

## Slide 29: Smooth first, then derivative

## Slide 30: Smooth first, then derivative

## Slide 31: Smooth first, then derivative

## Slide 32: Sobel filter! Smooth & derivative

## Slide 33: Image derivatives
Recall:
Want smoothing too!

## Slide 34: Finding edges
Could take derivative
Find high responses
Sobel filters!
But let’s stop a moment get
some basics

## Slide 35
The gradient direction is give
How does this relate to the direction of the edge?
Simplest image gradient
How would you implement this as a filter?
perpendicular
0 -1 1
The edge strength is given by the gradient magnitude

## Slide 36
Sobel operator
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
-1 | -2 | -1
0 | 0 | 0
1 | 2 | 1
Magnitude:
Orientation:
In practice, it is common to use:
What’s the C/C++ function?
Use atan2
Who was Sobel?
Irwin Sobel (born 1940)
Consultant (HP Labs Retired –
8Mar13) · Computer Vision & Graphics

## Slide 37: Finding edges
Could take derivative
Find high responses
Sobel filters!
But…
Edges go both ways
Want to find extrema

## Slide 38: 2nd derivative!
Crosses zero at extrema

## Slide 39: Laplacian (2nd derivative)!
Crosses zero at extrema
Recall:
Laplacian:
Again, have to estimate f’’(x):

## Slide 40: Laplacians
Laplacian:

## Slide 41: Laplacians
Laplacian:
Measures the divergence of the gradient
  Flux of gradient vector field through small area

## Slide 49: Laplacians
Laplacian:

## Slide 50: Laplacians
Laplacian:

## Slide 51: Laplacians
Laplacian:

## Slide 52: Laplacians
Laplacian:

## Slide 53: Laplacians
Laplacian:
Negative Laplacian, -4 in middle
Positive Laplacian --->

## Slide 54: Laplacians also sensitive to noise
Again, use gaussian smoothing
Can just use one kernel since convs commute
Laplacian of Gaussian, LoG
Can get good approx. with 5x5 - 9x9 kernels

## Slide 55: Another edge detector:
Image is a function:
  Has high frequency and low frequency components
  Think in terms of fourier transform
Edges are high frequency changes
Maybe we want to find edges of a specific size (i.e. specific frequency)

## Slide 56: Difference of Gaussian (DoG)
Gaussian is a low pass filter
Strongly reduce components with frequency f < σ
(g*I) low frequency components
I - (g*I) high frequency components
g(σ1)*I - g(σ2)*I
  Components in between these frequencies
g(σ1)*I - g(σ2)*I = [g(σ1) - g(σ2)]*I

## Slide 57: Difference of Gaussian (DoG)
g(σ1)*I - g(σ2)*I = [g(σ1) - g(σ2)]*I
=
σ = 2
σ = 1

## Slide 58: Difference of Gaussian (DoG)
g(σ1)*I - g(σ2)*I = [g(σ1) - g(σ2)]*I
This looks a lot like our LoG!
(not actually the same but similar)

## Slide 59: DoG (1 - 0)

## Slide 60: DoG (2 - 1)

## Slide 61: DoG (3 - 2)

## Slide 62: DoG (4 - 3)

## Slide 63: Another approach: gradient magnitude
Don’t need 2nd derivatives
Just use magnitude of gradient

## Slide 64: Another approach: gradient magnitude
Don’t need 2nd derivatives
Just use magnitude of gradient
Are we done? No!

## Slide 65: Another approach: gradient magnitude
Don’t need 2nd derivatives
Just use magnitude of gradient
Are we done? No!

## Slide 66: What we really want: line drawing

## Slide 67: Canny Edge Detection http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/
Your first image processing pipeline!
  Old-school CV is all about pipelines
Algorithm:
1. Smooth image (only want “real” edges, not noise)
2. Calculate gradient direction and magnitude
3. Non-maximum suppression perpendicular to edge
4. Threshold into strong, weak, no edge
5. Connect together components

## Slide 68: Smooth image http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/
You know how to do this, gaussians!

## Slide 69: Gradient magnitude and direction http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/
Sobel filter

## Slide 70: Non-maximum suppression http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/
Want single pixel edges, not thick blurry lines
Need to check nearby pixels
See if response is highest

## Slide 71: Non-maximum suppression

## Slide 72: Non-maximum suppression

## Slide 73: Non-maximum suppression

## Slide 74: Non-maximum suppression

## Slide 75: Non-maximum suppression

## Slide 76: Non-maximum suppression

## Slide 77: Non-maximum suppression

## Slide 78: Non-maximum suppression http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/

## Slide 79: Threshold edges http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/
Still some noise
Only want strong edges
2 thresholds T and t, 3 cases
  R > T: strong edge
  R < T but R > t: weak edge
  R < t: no edge
Why two thresholds?

## Slide 80: Connect ‘em up! http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/
Strong edges are edges!
Weak edges are edges iff they connect to strong
Look in some neighborhood (usually 8 closest)

## Slide 81: Canny Edge Detection http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/
Your first image processing pipeline!
  Old-school CV is all about pipelines
Algorithm:
Smooth image (only want “real” edges, not noise)
Calculate gradient direction and magnitude
Non-maximum suppression perpendicular to edge
Threshold into strong, weak, no edge
Connect together components
Tunable: Sigma, thresholds

## Slide 82: Canny Edge Detection http://bigwww.epfl.ch/demo/ip/demos/edgeDetector/

## Slide 83: Canny on Kidney

## Slide 84: Canny Characteristics
The Canny operator gives single-pixel-wide images with good continuation between adjacent pixels
It is the most widely used edge operator today; no one has done better since it came out in the late 80s. Many implementations are available.
It is very sensitive to its parameters, which need to be adjusted for different application domains.

## Slide 85: An edge is not a line...
How can we detect lines ?

## Slide 86: Finding lines in an image
Option 1:
  Search for the line at every possible position/orientation
  What is the cost of this operation?
Option 2:
  Use a voting scheme: Hough transform

## Slide 87: Finding lines in an image
Connection between image (x,y) and Hough (m,b) spaces
  A line in the image corresponds to a point in Hough space
  To go from image space to Hough space:
    given a set of points (x,y), find all (m,b) such that y = mx + b
x
y
m
b
m0
b0
image space
Hough space

## Slide 88: Hough transform algorithm
Typically use a different parameterization
  d is the perpendicular distance from the line to the origin
   is the angle of this perpendicular with the horizontal.

## Slide 89: Hough transform algorithm
Basic Hough transform algorithm
  Initialize H[d, ]=0
  for each edge point I[x,y] in the image
    compute gradient magnitude m and angle 
      H[d, ] += 1
  Find the value(s) of (d, ) where H[d, ] is maximum
  The detected line in the image is given by
  Complexity?
d

Array H

## Slide 90: How do you extract the line segments from the accumulators?
pick the bin of H with highest value V
while V > value_threshold {
order the corresponding pointlist from PTLIST
merge in high gradient neighbors within 10 degrees
create line segment from final point list
zero out that bin of H
pick the bin of H with highest value V }

## Slide 91: Example
0 0 0 100 100
0 0 0 100 100
0 0 0 100 100
100 100 100 100 100
100 100 100 100 100
- - 0 0 -
- - 0 0 -
90 90 40 20 -
90 90 90 40 -
- - - - -
- - 3 3 -
- - 3 3 -
3 3 3 3 -
3 3 3 3 -
- - - - -
360
.
6
3
0
- - - - - - -
- - - - - - -
- - - - - - -
4 - 1 - 2 - 5
- - - - - - -
0 10 20 30 40 …90
360
.
6
3
0
- - - - - - -
- - - - - - -
- - - - - - -
* - * - * - *
- - - - - - -
(1,3)(1,4)(2,3)(2,4)
(3,1)
(3,2)
(4,1)
(4,2)
(4,3)
gray-tone image
DQ
THETAQ
Accumulator H
PTLIST
distance
angle

## Slide 92: Line segments from Hough Transform

## Slide 93: Extensions
Extension 1: Use the image gradient (we just did that)
Extension 2
  give more votes for stronger edges
Extension 3
  change the sampling of (d, ) to give more/less resolution
Extension 4
  The same procedure can be used with circles, squares, or any other shape, How?
Extension 5; the Burns procedure. Uses only angle, two different quantifications, and connected components with votes for larger one.
Notes: Ask: what are the axes for a circle Hough space? What does a point in the image map to in the Hough space?

## Slide 94
Chalmers University
of Technology

## Slide 95
Chalmers University
of Technology

## Slide 96: Hough Transform for Finding Circles
Equations:
r = r0 + d sin 
c = c0 - d cos 
r, c, d are parameters
Main idea: The gradient vector at an edge pixel points
to the center of the circle.
*(r,c)
d

## Slide 97: Why it works
Filled Circle:
Outer points of circle have gradient
direction pointing to center.
Circular Ring:
Outer points gradient towards center.
Inner points gradient away from center.
The points in the away direction don’t
accumulate in one bin!

## Slide 99: Finding lung nodules (Kimme & Ballard)

## Slide 100: Finale
Edge operators are based on estimating derivatives.
While first derivatives show approximately where the edges are, zero crossings of second derivatives were shown to be better.
Ignoring that entirely, Canny developed his own edge detector that everyone uses now.
After finding good edges, we have to group them into lines, circles, curves, etc. to use further.
The Hough transform for circles works well, but for lines the performance can be poor. The Burns operator or some tracking operators (old ORT pkg) work better.