## Slide 1: Computer Vision CSE 455 Stereo and 3D Linda Shapiro Professor of Computer Science & Engineering Professor of Electrical Engineering

## Slide 2: Camera Calibration
The idea is to snap
images at different
depths and get a
lot of 2D-3D point
correspondences.
x1, y1, z1, u1, v1
x2, y2, z1, u2, v2
.
.
xn, yn, zn, un, vn
Then solve a system
of equations to get
camera parameters.

## Slide 3: Camera Parameters
A camera is described by several parameters
Translation T of the optical center from the origin of world coords
Rotation R of the image plane
focal length f, principal point (x’c, y’c), pixel size (sx, sy)
blue parameters are called “extrinsics,” red are “intrinsics”
The definitions of these parameters are not completely standardized
especially intrinsics—varies from one book to another
Projection equation
The projection matrix models the cumulative effect of all parameters
Useful to decompose into a series of operations
projection
intrinsics
rotation
translation
identity matrix
[tx, ty, tz]T

## Slide 4: Stereo

## Slide 6: Amount of horizontal movement is …
…inversely proportional to the distance from the camera

## Slide 7: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
f
x
x’
Baseline B
z
C
C’
X
f
X
x
x'

## Slide 8: Depth from disparity
f
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth.
x
See Chapter 12 of Shapiro and Stockman Text.

## Slide 9: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
Sub-Problems
  Calibration: How do we recover the relation of the cameras (if not already known)?
  Correspondence: How do we search for the matching point x’?
X
x
x'

## Slide 10: Correspondence Problem
We have two images taken from cameras with different intrinsic and extrinsic parameters
How do we match a point in the first image to a point in the second? How can we constrain our search?
x
?

## Slide 11: Key idea: Epipolar constraint
Potential matches for x have to lie on the corresponding line l’.
Potential matches for x’ have to lie on the corresponding line l.
x
x’
X
x’
X
x’
X

## Slide 12: Epipolar geometry: notation
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers
X
x
x’

## Slide 13: Epipolar geometry: notation
Epipolar Lines - intersections of epipolar plane with image planes (always come in corresponding pairs)
X
x
x’
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers

## Slide 14: Example: Converging cameras

## Slide 15: Example: Motion parallel to image plane

## Slide 16: Epipolar constraint: Calibrated case
X
x
x’
Assume that the intrinsic and extrinsic parameters of the cameras are known
We can multiply the projection matrix of each camera (and the image points) by the inverse of the calibration matrix to get normalized image coordinates
We can also set the global coordinate system to the coordinate system of the first camera. Then the projection matrices of the two cameras can be written as [I | 0] and [R | t]

## Slide 17: Simplified Matrices for the 2 Cameras
= (R | T)

## Slide 18: Epipolar constraint: Calibrated case
X
x
x’ = Rx+t
R
t
The vectors Rx, t, and x’ are coplanar
= (x,1)T
Notes: X’ is X in the second camera’s coordinate system
We can identify the non-homogeneous 3D vectors X and X’ with the homogeneous coordinate vectors x and x’ of the projections of the two points into the two respective images

## Slide 19: Epipolar constraint: Calibrated case
Essential Matrix E
(Longuet-Higgins, 1981)
X
x
x’
The vectors Rx, t, and x’ are coplanar

## Slide 20: Epipolar constraint: Calibrated case
X
x
x’
E x is the epipolar line associated with x (l' = E x)
ETx' is the epipolar line associated with x' (l = ETx')
E e = 0 and ETe' = 0
E is singular (rank two)
E has five degrees of freedom

## Slide 21: Moving on to stereo…
Fuse a calibrated binocular stereo pair to produce a depth image
image 1
image 2
Dense depth map
Many of these slides adapted from Steve Seitz and Lana Lazebnik

## Slide 22: Stereo image rectification
Reproject image planes onto a common plane parallel to the line between camera centers
Pixel motion is horizontal after this transformation
Two homographies (3x3 transform), one for each input image reprojection
C. Loop and Z. Zhang. Computing Rectifying Homographies for Stereo Vision. IEEE Conf. Computer Vision and Pattern Recognition, 1999.

## Slide 23: Example
Unrectified
Rectified

## Slide 24
Matching cost
disparity
Left
Right
scanline
Slide a window along the right scanline and compare contents of that window with the reference window in the left image
Matching cost: SSD, SAD, or normalized correlation

## Slide 25: Correspondence search
Left
Right
scanline
Norm. corr

## Slide 26: Results with window search
Window-based matching
Ground truth
Data

## Slide 27: Using more than two images
Multi-View Stereo for Community Photo Collections M. Goesele, N. Snavely, B. Curless, H. Hoppe, S. Seitz Proceedings of ICCV 2007,

## Slide 28: 3D model
“Digital copy” of real object
Allows us to
  Inspect details of object
  Measure properties
  Reproduce in different material
Many applications
  Cultural heritage preservation
  Computer games and movies
  City modelling
  E-commerce

## Slide 29: Applications: cultural heritage
SCULPTEUR European project
Notes: To sum up,

## Slide 30: Applications: art
Domain Series Domain VIII Crouching 1999 Mild steel bar 81 x 59 x 63 cm
Block Works Precipitate III 2004 Mild steel blocks 80 x 46 x 66 cm

## Slide 31: Applications: structure engineering
BODY / SPACE / FRAME, Antony Gormley, Lelystad, Holland
Notes: To sum up,

## Slide 32: Applications: 3D indexation
SCULPTEUR European project
medical, industrial and cultural heritage indexation
? ?
? ? ?
?
? ?
?

## Slide 33: Applications: archaeology
1186 fragments
“forma urbis romae” project
Fragments of the City: Stanford's Digital Forma Urbis Romae Project David Koller, Jennifer Trimble, Tina Najbjerg, Natasha Gelfand, Marc Levoy Proc. Third Williams Symposium on Classical Architecture, Journal of Roman Archaeology supplement, 2006.

## Slide 34: Applications: large scale modelling
[Pollefeys08]
[Furukawa10]
[Goesele07]
[Cornelis08]

## Slide 35: Applications: Medicine

## Slide 36: Scanning technologies
Laser scanner, coordinate measuring machine
  Very accurate
  Very Expensive
  Complicated to use
Minolta
Contura CMM
“Michelangelo” project

## Slide 37: Medical Scanning System

## Slide 38: The “Us” Data Set (subset)

## Slide 39: 3d shape from photographs
“Estimate a 3d shape that would generate the input photographs given the same material, viewpoints and illumination”
material
illumination
viewpoint
geometry
image
?

## Slide 40: Photometric Stereo
Estimate the surface normals of a given scene given multiple 2D images taken from the same viewpoint, but under different lighting conditions.
Basic photometric stereo required a Lambertian reflectance model:
I =  n · v
where I is pixel intensity, n is the normal, v is the lighting direction, and  is diffuse albedo constant, which is a reflection coefficient.

## Slide 41: Basic Photometric Stereo

## Slide 42: Basic Photometric Stereo

## Slide 43: Basic Photometric Stereo
K light sources
Lead to K images R1(p,q), ...,RK(p,q) each from just one of the light sources being on
For any (p,q), we get K intensities I1,...IK
Leads to a set of linear equations of the form
Ik = nvk
Solving leads to a surface normal map.

## Slide 44: Photometric Stereo
Inputs
3D normals

## Slide 45: 3d shape from photographs
Photograph based 3d reconstruction is:
  practical
  fast
  non-intrusive
  low cost
  Easily deployable outdoors
  “low” accuracy
  Results depend on material properties

## Slide 46: Reconstruction
Generic problem formulation: given several images of the same object or scene, compute a representation of its 3D shape

## Slide 47: Reconstruction
Generic problem formulation: given several images of the same object or scene, compute a representation of its 3D shape
“Images of the same object or scene”
  Arbitrary number of images (from two to thousands)
  Arbitrary camera positions (camera network or video sequence)
  Calibration may be initially unknown
“Representation of 3D shape”
  Depth maps
  Meshes
  Point clouds
  Patch clouds
  Volumetric models
  Layered models

## Slide 48: Multiple-baseline stereo
I1
I2
I10
M. Okutomi and T. Kanade, “A Multiple-Baseline Stereo System,” IEEE Trans. on Pattern Analysis and Machine Intelligence, 15(4):353-363 (1993).

## Slide 49: Reconstruction from silhouettes
Can be computed robustly
Can be computed efficiently
-
=
background
+
foreground
background
foreground

## Slide 50: Reconstruction from Silhouettes
Binary Images
The case of binary images: a voxel is photo-consistent if it lies inside the object’s silhouette in all views

## Slide 51: Reconstruction from Silhouettes
Binary Images
Finding the silhouette-consistent shape (visual hull):
  Backproject each silhouette
  Intersect backprojected volumes
The case of binary images: a voxel is photo-consistent if it lies inside the object’s silhouette in all views
voxel space

## Slide 52: Calibrated Image Acquisition
Calibrated Turntable
360° rotation (21 images)
Selected Dinosaur Images
Selected Flower Images

## Slide 53: Space Carving in General
Space Carving Algorithm
Image 1
Image N
…...
  Initialize to a volume V containing the true scene
  Choose a voxel on the outside of the volume
  Carve if not photo-consistent (inside object’s silhouette)
  Project to visible input images
K. N. Kutulakos and S. M. Seitz, A Theory of Shape by Space Carving, ICCV 1999

## Slide 54: Our 4-camera light-striping stereo system
projector
rotation
table
cameras
3D
object
(now deceased)

## Slide 55: Calibration Object
The idea is to snap
images at different
depths and get a
lot of 2D-3D point
correspondences.

## Slide 60
image plane
depth map
(u,v,d)
OUTSIDE
one of many cubes
in virtual 3D cube space
3D space is made up of many cubes.
(x,y,z)
(

## Slide 69: More: Space Carving Results: African Violet
Input Image (1 of 45)
Reconstruction
Reconstruction
Reconstruction
Source: S. Seitz

## Slide 70: More: Space Carving Results: Hand
Input Image
(1 of 100)
Views of Reconstruction

## Slide 71: Stereo from community photo collections
Up to now, we’ve always assumed that camera calibration is known
For photos taken from the Internet, we need structure from motion techniques to reconstruct both camera positions and 3D points.

## Slide 73: Head Reconstruction from Uncalibrated Internet Photos
Input: Internet photos in different poses and expressions
Output: 3D model of the head
work of
Shu Liang

## Slide 74: Recognizing Deformable Shapes
Salvador Ruiz Correa
(CSE/EE576 Computer Vision I)

## Slide 75: Goal
We are interested in developing algorithms for recognizing and classifying deformable object shapes from range data.
3-D Output
Surface Mesh
3-D Laser Scanner
Input
3-D
Object
This is a difficult problem that is relevant in several application fields.
Range
data
(Cloud of
3-D points)
Post-
processing

## Slide 76: What Kind Of Deformations?
Toy animals
3-D Faces
Normal
Mandibles
Neurocranium
Normal
Abnormal
Abnormal
Shape classes: significant
amount of intra-class variability

## Slide 77: Component-Based Methodology
Numeric
Signatures
Components
Symbolic
Signatures
Architecture
of
Classifiers
+
Recognition And Classification Of
Deformable Shapes
Overcomes the limitations
of the alignment-verification
approach
define
Describe
spatial
configuration
1
2
3
4

## Slide 78: Numeric Signatures
Architecture
of
Classifiers
Numeric
Signatures
Components
Symbolic
Signatures
4
+
1
2
3
Encode Local
Surface Geometry of an Object

## Slide 79: The Spin Image Signature
P
X
n


P is the selected vertex.
X is a contributing point
of the mesh.
 is the perpendicular distance from X to P’s surface normal.
 is the signed perpendicular distance from X to P’s tangent plane.
tangent plane at P

## Slide 80: Spin Image Construction
A spin image is constructed
- about a specified oriented point o of the object surface
- with respect to a set of contributing points C, which is
controlled by maximum distance and angle from o.
It is stored as an array of accumulators S(,) computed via:
For each point c in C(o)
1. compute  and  for c.
2. increment S (,)
o

## Slide 81: Numeric Signatures: Spin Images
Rich set of surface shape descriptors.
Their spatial scale can be modified to include local and non-local surface features.
Representation is robust to scene clutter and occlusions.
P
Spin images for point P
3-D faces

## Slide 82: Components
Numeric
Signatures
Components
Symbolic
Signatures
Architecture
of
Classifiers
4
+
1
2
3
Equivalent Numeric Signatures:
Encode Local Geometry
of a Shape Class
define

## Slide 83: How To Extract Shape Class Components?
…
…
Component
Detector
Compute
Numeric
Signatures
Training Set
Select
Seed
Points
Region
Growing
Algorithm
Grown components
around seeds

## Slide 84: Component Extraction Example
Labeled
Surface Mesh
Selected 8 seed
points by hand
Region
Growing
Grow one region at the time
(get one detector
per component)
Detected
components on a
training sample

## Slide 85: How To Combine Component Information?
…
Extracted components on test samples
1
2
3
7
6
4
8
5
1
1
1
2
2
2
2
2
2
Note: Numeric signatures are invariant to mirror symmetry;
our approach preserves such an invariance.

## Slide 86: Symbolic Signatures
Numeric
Signatures
Components
Symbolic
Signatures
Architecture
of
Classifiers
4
+
1
2
3
Encode Geometrical
Relationships
Among Components

## Slide 87: Symbolic Signature
Symbolic
Signature at P
3
4
5
6
8
7
Labeled
Surface Mesh
Matrix storing component
labels
Encode
Geometric
Configuration
Critical
Point P

## Slide 88: Symbolic Signatures Are Robust To Deformations
P
3
4
5
6
7
8
3
3
3
3
4
4
4
4
8
8
8
8
5
5
5
5
6
6
6
7
7
7
7
6
Relative position of components is stable across deformations: experimental evidence

## Slide 89: Architecture of Classifiers
Numeric
Signatures
Components
Symbolic
Signatures
Architecture
of
Classifiers
4
+
1
2
3
Learns Components
And Their
Geometric Relationships

## Slide 90: Proposed Architecture
Input
Labeled
Mesh
Class
Label
-1
(Abnormal)
Verify spatial configuration
of the components
Identify
Symbolic
Signatures
Identify
Components
Two classification stages
Surface
Mesh

## Slide 91: Experimental Validation
Recognition Tasks: 4 (T1 - T4)
Classification Tasks: 3 (T5 – T7)
No. Experiments: 5470
Setup
Recognition
Classification
Laser
Rotary Table

## Slide 92: Shape Classes

## Slide 93
Enlarging Training Sets Using Virtual Samples
Displacement
Vectors
Originals
Morphs
Twist (5deg)
+ Taper
- Push
+ Spherify (10%)
Push
+Twist (10 deg)
+Scale (1.2)
Original
Global Morphing
Operators
Morphs
Physical Modeling
(14)
University of Washington
Electrical Engineering

## Slide 94: Task 1: Recognizing Single Objects (1)
No. Shape classes: 9.
Training set size: 400 meshes.
Testing set size: 200 meshes.
No. Experiments: 1960.
No. Component detectors:3.
No. Symbolic signature detectors: 1.
Numeric signature size: 40x40.
Symbolic signature size: 20x20.
No clutter and occlusion.

## Slide 95: Task 1: Recognizing Single Objects (2)
Snowman: 93%.
Rabbit: 92%.
Dog: 89%.
Cat: 85.5%.
Cow: 92%.
Bear: 94%.
Horse: 92.7%.
Human head: 97.7%.
Human face: 76%.
Recognition rates (true positives)
(No clutter, no occlusion, complete models)

## Slide 96: Main Contributions (2)
A region growing algorithm for learning shape class components.
A novel architecture of classifiers for abstracting the geometry of a shape class.
A validation of our methodology in a set of large scale recognition and classification experiments aimed at applications in scene analysis and medical diagnosis.