## Slide 1: Multi-view stereo
Many slides adapted from S. Seitz, Y. Furukawa, N. Snavely

## Slide 2: Multi-view stereo
Goal: given several images of the same object or scene, compute a representation of its 3D shape
Source: C. Hernandez, N. Snavely

## Slide 3: Multi-view stereo
Goal: given several images of the same object or scene, compute a representation of its 3D shape
“Images of the same object or scene”
  Arbitrary number of images (from two to thousands)
  Arbitrary camera positions (special rig, camera network or video)
  Calibration may be known or unknown

## Slide 4: Multi-view stereo
Goal: given several images of the same object or scene, compute a representation of its 3D shape
“Images of the same object or scene”
  Arbitrary number of images (from two to thousands)
  Arbitrary camera positions (special rig, camera network or video)
  Calibration may be known or unknown
“Representation of 3D shape”
  Depth maps
  Meshes
  Point clouds
  Patch clouds
  Volumetric models
  Signed distance functions, light fields

## Slide 5: Outline
Applications and motivation
Plane sweep stereo
Depth map fusion
Patch-based multi-view stereo (PMVS)
Stereo from Internet photo collections
Recent trends

## Slide 6: Applications
Source: N. Snavely

## Slide 7: Applications
Source: N. Snavely

## Slide 8: Applications
Source: N. Snavely

## Slide 9: Applications
Enable inspection in hard to reach areas with drone photos and 3D reconstruction
Create 3D model from images
Provide tools to inspect on images and map interactions to 3D
Source: D. Hoiem

## Slide 10: Multi-view stereo: Basic idea
Source: Y. Furukawa

## Slide 11: Multi-view stereo: Basic idea
Source: Y. Furukawa

## Slide 12: Multi-view stereo: Basic idea
Source: Y. Furukawa

## Slide 13: Multi-view stereo: Basic idea
Source: Y. Furukawa

## Slide 14: Why MVS?
Different points on the object’s surface will be more clearly visible in some subset of cameras
  Could have high-res closeups of some regions
  Some surfaces are foreshortened from certain views
  Some points may be occluded entirely in certain views
Source: N. Snavely

## Slide 15
Cameras 4 and 5 can more clearly see point p
p
Source: N. Snavely
1
2
3
4
5

## Slide 16
q
Cameras 3 and 4 can more clearly see point q
Source: N. Snavely
1
2
3
4
5

## Slide 17
Camera 5 can’t see point r
1
2
3
4
5
r
Source: N. Snavely

## Slide 18
Camera 1 can’t see point s
1
2
3
4
5
s
Source: N. Snavely

## Slide 19: Why MVS?
Different points on the object’s surface will be more clearly visible in some subset of cameras
  Could have high-res closeups of some regions
  Some surfaces are foreshortened from certain views
  Some points may be occluded entirely in certain views
More measurements per point can reduce error
Source: N. Snavely

## Slide 20
Source: N. Snavely
More measurements reduce triangulation error

## Slide 21
Source: N. Snavely
More measurements reduce triangulation error

## Slide 22: Outline
Applications and motivation
Plane sweep stereo
Depth map fusion

## Slide 23: Plane sweep stereo
reference camera
input image
input image
Sweep plane across a range of depths w.r.t. a reference camera
  For each depth, project each input image onto that plane (homography) and compare the resulting stack of images
R. Collins, A space-sweep approach to true multi-image matching, CVPR 1996

## Slide 24: Plane sweep stereo
Sweep plane across a range of depths w.r.t. a reference camera
  For each depth, project each input image onto that plane (homography) and compare the resulting stack of images
input image
R. Collins, A space-sweep approach to true multi-image matching, CVPR 1996
input image
reference camera

## Slide 25: Plane sweep stereo: Key idea
Image 1
Image 2
Sweeping plane
Scene surface
Reference image

## Slide 26: Plane sweep stereo: Key idea
Image 1
Image 2

## Slide 27: Plane sweep stereo: Key idea
Image 1
Image 2

## Slide 28: Plane sweep stereo: Key idea
Image 1
Image 2

## Slide 29: Plane sweep stereo: Key idea
Image 1
Image 2

## Slide 30: Plane sweep stereo: Key idea
Image 1
Image 2

## Slide 31: Plane sweep stereo: Key idea
Image 1
Image 2
Reference image
✓

## Slide 32: Plane sweep stereo: Fast implementation
For each depth plane
  Compute homographies projecting each image onto that depth plane
  For each pixel in the composite image stack, compute the variance
For each pixel, select the depth that gives the lowest variance
R. Yang and M. Pollefeys, Multi-Resolution Real-Time Stereo on Commodity Graphics Hardware, CVPR 2003

## Slide 33: Merging depth maps
Given a group of images, compute a depth map using each view as a reference
Merge multiple depth maps into a volume or a mesh (see, e.g., Curless and Levoy, 1996)
Map 1
Map 2
Merged

## Slide 34: Volumetric fusion
Source: N. Snavely

## Slide 35: Volumetric fusion
Source: N. Snavely

## Slide 36: Fast depth map fusion using height maps
Start with a cluster of registered views (from SFM on Internet photo collections)
J.-M. Frahm et al., Building Rome on a Cloudless Day, ECCV 2010
D. Gallup et al. 3D Reconstruction using an n-Layer Heightmap. DAGM 2010
Notes: stereo is same as for video just NCC instead of SAD

## Slide 37: Fast depth map fusion using height maps
Obtain a (noisy) depth map for every view using plane sweeping stereo with normalized cross-correlation
far
near
J.-M. Frahm et al., Building Rome on a Cloudless Day, ECCV 2010
D. Gallup et al. 3D Reconstruction using an n-Layer Heightmap. DAGM 2010
Notes: stereo is same as for video just NCC instead of SAD

## Slide 38: Fast depth map fusion using height maps
Enforces vertical facades
One continuous surface, no holes
Fast to compute, low memory complexity
J.-M. Frahm et al., Building Rome on a Cloudless Day, ECCV 2010
D. Gallup et al. 3D Reconstruction using an n-Layer Heightmap. DAGM 2010

## Slide 39: Fast depth map fusion using height maps
YouTube Video
J.-M. Frahm et al., Building Rome on a Cloudless Day, ECCV 2010

## Slide 40: Outline
Applications and motivation
Plane sweep stereo
Depth map fusion
Patch-based multi-view stereo (PMVS)
Stereo from Internet photo collections

## Slide 41: Patch-based multi-view stereo (PMVS)
Detect keypoints
Triangulate a sparse set of initial matches
Iteratively expand matches to nearby locations
Use visibility constraints to filter out false matches
Perform surface reconstruction
Y. Furukawa and J. Ponce, Accurate, Dense, and Robust Multi-View Stereopsis, CVPR 2007.
PMVS software

## Slide 42: Patch-based multi-view stereo (PMVS)
Y. Furukawa and J. Ponce, Accurate, Dense, and Robust Multi-View Stereopsis, CVPR 2007.
PMVS software

## Slide 43: Stereo from community photo collections
Need structure from motion to recover unknown camera parameters
Need view selection to find good groups of images on which to run dense stereo

## Slide 44: Local view selection
M. Goesele et al., Multi-View Stereo for Community Photo Collections, ICCV 2007

## Slide 45: Local view selection
M. Goesele et al., Multi-View Stereo for Community Photo Collections, ICCV 2007

## Slide 46: Local view selection
M. Goesele et al., Multi-View Stereo for Community Photo Collections, ICCV 2007

## Slide 47: Local view selection
M. Goesele et al., Multi-View Stereo for Community Photo Collections, ICCV 2007
Notre Dame de Paris
653 images 313 photographers

## Slide 48: Local view selection
M. Goesele et al., Multi-View Stereo for Community Photo Collections, ICCV 2007

## Slide 49: Local view selection
M. Goesele et al., Multi-View Stereo for Community Photo Collections, ICCV 2007
Model merged from 72 depth maps
Model from 56 depth maps with laser scan overlaid
(90% of points within 0.25% of ground truth)

## Slide 50: Towards Internet-scale multi-view stereo
Y. Furukawa, B. Curless, S. Seitz and R. Szeliski, Towards Internet-scale Multi-view Stereo, CVPR 2010

## Slide 51: Towards Internet-scale multi-view stereo
YouTube video, CMVS software
Y. Furukawa, B. Curless, S. Seitz and R. Szeliski, Towards Internet-scale Multi-view Stereo, CVPR 2010

## Slide 52: The Visual Turing Test for scene reconstruction
Q. Shan, R. Adams, B. Curless, Y. Furukawa, and S. Seitz, The Visual Turing Test for Scene Reconstruction, 3DV 2013. YouTube video
Notes: Abstract: We present the first large scale system for capturing and rendering relightable scene reconstructions from massive unstructured photo collections taken under different illumination conditions and viewpoints. We combine photos taken from many sources, Flickr-based ground-level imagery, oblique aerial views, and streetview, to recover models that are significantly more complete and detailed than previously demonstrated. We demonstrate the ability to match both the viewpoint and illumination of arbitrary input photos, enabling a Visual Turing Test in which photo and rendering are viewed side-by-side and the observer has to guess which is which. While we cannot yet fool human perception, the gap is closing.

## Slide 53: Last time: Multi-view stereo
Applications and motivation
Plane sweep stereo
Depth map fusion
Patch-based multi-view stereo (PMVS)
Stereo from Internet photo collections

## Slide 54: COLMAP MVS
J. Schonberger et al. Pixelwise View Selection for Unstructured Multi-View Stereo. ECCV 2016
Results video

## Slide 55: Outline
Applications and motivation
Plane sweep stereo
Patch-based multi-view stereo (PMVS)
Stereo from Internet photo collections
Recent trends, deep learning approaches

## Slide 56: Ongoing research directions
Challenging lighting conditions
Indoor modeling
Ground/aerial
Dynamic reconstruction

## Slide 57: Deep learning for MVS
Y. Yao et al. MVSNet: Depth Inference for Unstructured Multi-view Stereo. ECCV 2018
Notes: We present an end-to-end deep learning architecture for depth map inference from multi-view images. In the network, we first extract deep visual image features, and then build the 3D cost volume upon the reference camera frustum via the differentiable homography warping. Next, we apply 3D convolutions to regularize and regress the initial depth map, which is then refined with the reference image to generate the final output. Our framework flexibly adapts arbitrary N-view inputs using a variance-based cost metric that maps multiple features into one cost feature. The proposed MVSNet is demonstrated on the large-scale indoor DTU dataset. With simple post-processing, our method not only significantly outperforms previous state-of-the-arts, but also is several times faster in runtime. We also evaluate MVSNet on the complex outdoor Tanks and Temples dataset, where our method ranks first before April 18, 2018 without any fine-tuning, showing the strong generalization ability of MVSNet.

## Slide 58: Deep learning for MVS
Y. Yao et al. MVSNet: Depth Inference for Unstructured Multi-view Stereo. ECCV 2018

## Slide 59: DUSt3R: Dense Unconstrained Stereo 3D Reconstruction
S. Wang et al. DUSt3R: Geometric 3D Vision Made Easy. CVPR 2024

## Slide 60: DUSt3R: Dense Unconstrained Stereo 3D Reconstruction
S. Wang et al. DUSt3R: Geometric 3D Vision Made Easy. CVPR 2024
Training data: 8.5M image pairs with reference 3D
Training objective: fully supervised 3D regression (scale-normalized, weighted by confidence)

## Slide 61: DUSt3R: Dense Unconstrained Stereo 3D Reconstruction
S. Wang et al. DUSt3R: Geometric 3D Vision Made Easy. CVPR 2024

## Slide 62: DUSt3R: Dense Unconstrained Stereo 3D Reconstruction
S. Wang et al. DUSt3R: Geometric 3D Vision Made Easy. CVPR 2024
Reconstruction from nearly opposite viewpoints

## Slide 63: MAST3R: Matching and Stereo 3D Reconstruction
V. Leroy et al. Grounding image matching in 3D with MASt3R. ECCV 2024

## Slide 64: MAST3R: Matching and Stereo 3D Reconstruction
V. Leroy et al. Grounding image matching in 3D with MASt3R. ECCV 2024

## Slide 65: MAST3R: Matching and Stereo 3D Reconstruction

## Slide 66: MAST3R: Matching and Stereo 3D Reconstruction